KEY HANDY INFO

| Ast = Mu x 103 -------------------- .8 x .85 jd Fsy (= 500/450?) | Def = 5wL4 x 10-3 -------------------- 384 x E x I |
| --- | --- |
| LIVE LOAD – BALCONIES : Houses 2.0kPa Other As per area providing access but not less than 4.0kPa Roof = 0.25kPa or 1.8 + 0.12 kPa ---- A SINGLE SS SPAN > M = WL2/8 HALF SS SPAN = 1/4M (L2) SINGLE FXD SPAN > M = WL2/12 ENDS WL2/24 MIDSPAN DOUBLE SS SPAN > M = WL2/8 MID SUPPORT WL2/14 MID SPAN DOUBLE FXD SPAN > M = WL2/12 SUPPORTS WL2/24 MID SPAN | REO BAR Bar R6 F8 R10 F11 N12 N16 N20 N24 N28 N32 Area 31 50 80 95 110 200 310 450 620 800 Beam Laps 450 600 600 750 900 1200 1800 2100 Column Laps 450 600 750 900 1000 1200 Cogs 120 150 175 200 225 275 325 350 BAR AND MESH AREAS – SEE BELOW |